| CC 1000 |
| --- |
|  | Capacity Asphalt up to 455 m2/h Soil up to 130 m3/h Specifications Operating mass (incl. ROPS) 1650 kg Front module mass 810 kg Rear module mass 840 kg Max. operating mass 1730 kg Static linear load std/max front/rear 8,1/8,4 kg/cm Centrifugal force 17 kN Propulsion Both drums Water tank 105 litres Frequency/Amplitude 70 Hz/0,35 mm Speed 0-9 km/h Curb clearance 465 mm Engine Rated power, SAE J1995, at 2600 rpm 17 kW Model Perkins 403C-11 Dimensions Drum diameter 584 mm Length, w/w.o ROPS 2095/2040 mm Height, w/w.o ROPS 2300/1520 mm Drum width 1000 mm Drum shell thickness 13 mm Width, w/w.o ROPS 1070/1070 mm |  |

v